## Slide 1
Noodle2
Physical Design ECO Orchestration System
Yaakoub Elkhamra, PhD
January 2026

## Slide 2
What is Noodle2?
ECO Orchestration System for physical design timing closure
Automatically applies and evaluates **Engineering Change Orders**
Uses **parallel execution** with Ray for trial exploration
Implements **prior learning** to avoid ineffective ECOs
Supports **checkpoint/rollback** for robustness
All results from REAL OpenROAD execution - no mocking

## Slide 3
Technology Stack
Layer | Technology | Purpose
Orchestration | Noodle2 (Python) | ECO selection, survivor management
Parallelism | Ray | Distributed trial execution
EDA Engine | OpenROAD | Physical design, timing analysis
Build Flow | ORFS | Synthesis, placement, routing
PDKs | Nangate45, ASAP7, Sky130 | Process design kits

## Slide 4
OpenROAD - The EDA Engine
OpenSTA - Static Timing Analysis (WNS, TNS, hot_ratio)
TritonPlace - Global and detailed placement
FastRoute - Global routing
TritonRoute - Detailed routing
ReSizer - Gate sizing, buffer insertion
Production-quality, reproducible, open-source

## Slide 5
Ray - Distributed Parallel Execution
Single-Node Mode: 25 trials per stage in parallel
Utilizes all CPU cores (32 cores in demo)
Shared memory for ODB file access
Multi-Node Mode: Linear scaling with cluster
Fault tolerance for failed trials
Dashboard monitoring at http://localhost:8265

## Slide 6
ECO Types Supported
Category | ECOs
Topology Neutral | Cell Resize, Buffer Insert/Remove, Pin Swap
Placement Affecting | Timing-Driven Placement, Density Opt
Global/Aggressive | Full Optimization, Multi-Pass, VT Swap
Repair | Hold Repair, Clock Net Repair, Tie Fanout

## Slide 7
Study Execution Flow
1. **Base Case Verification** - Validate initial design metrics
2. **Stage Execution** - 20 stages with 25 trials each
3. **Survivor Selection** - Keep best performing variants
4. **Prior Learning** - Track ECO effectiveness
5. **Checkpoint/Rollback** - Save state, recover from degradation
6. **Visualization** - Generate heatmaps, trajectories
Total: 500 trials per study

## Slide 8
Nangate45
45nm Educational PDK

## Slide 9
Nangate45 - Design Setup
Property | Value
PDK | Nangate45 (45nm)
Design | Ibex RISC-V Core
Cell Count | ~10,000 cells
Clock Period | Aggressive constraints
ODB Size | 8.3 MB

## Slide 10
Nangate45 - Stage Progression
20 stages, funnel survivor selection (8 -> 2)

## Slide 11
Nangate45 - WNS Trajectory

## Slide 12
Nangate45 - Hot Ratio Trajectory

## Slide 13
Nangate45 - Final Results
Metric | Initial | Final | Improvement
WNS | -1848 ps | -1576 ps | +14.7%
hot_ratio | 0.523 | 0.149 | -71.6%

## Slide 14
ASAP7
7nm Predictive PDK

## Slide 15
ASAP7 - Design Setup
Property | Value
PDK | ASAP7 (7nm predictive)
Design | Ibex RISC-V Core
Cell Count | ~10,000 cells
Clock Period | Aggressive 7nm timing
ODB Size | ~10 MB

## Slide 16
ASAP7 - Stage Progression

## Slide 17
ASAP7 - WNS Trajectory

## Slide 18
ASAP7 - Final Results
Metric | Initial | Final | Improvement
WNS | -1067 ps | -1004 ps | +5.9%
hot_ratio | 0.55 | 0.004 | -99.3%

## Slide 19
Sky130 + Microwatt
130nm Open PDK + OpenPOWER Core

## Slide 20
Sky130 Microwatt - Design Setup
Property | Value
PDK | Sky130HD (130nm)
Design | Microwatt OpenPOWER Core
Cell Count | 162,637 cells
Clock Period | 4ns (250 MHz)
ODB Size | 95 MB

## Slide 21
Sky130 Microwatt - Stage Progression
Stage 6 (red): degradation detected but below rollback threshold

## Slide 22
Sky130 Microwatt - WNS Trajectory

## Slide 23
Sky130 Microwatt - Hot Ratio Trajectory
hot_ratio: 0.097 -> 0.0003 (99.7% reduction)

## Slide 24
Sky130 Microwatt - Final Results
Metric | Initial | Final | Improvement
WNS | -2989 ps | -1466 ps | +51.0%
hot_ratio | 0.097 | 0.0003 | -99.7%

## Slide 25
The 'Long Pole in the Tent' Problem
Observation: hot_ratio improved 99.7% but WNS only 51%
hot_ratio: Fraction of paths violating timing (9.7% -> 0.03%)
WNS: Worst single path's negative slack (-2989ps -> -1466ps)
Meaning:
We fixed 99.7% of all timing violations
But the single worst path only improved 51%
ONE stubborn path dominates WNS

## Slide 26
Why Does the Worst Path Resist?
Long combinational depth - Many logic stages in series
Placement-limited - Cells far apart, wire delay dominates
Technology limits - Already using max drive strength
Critical logic - Carry chains, multipliers, barrel shifters
Routing congestion - Detours adding wire delay
ECOs fix 'moderately bad' paths but struggle with 'truly terrible' ones

## Slide 27
Cross-PDK Comparison
PDK | Design | Cells | WNS Impr. | hot_ratio Red.
Nangate45 | Ibex | ~10K | +14.7% | -71.6%
ASAP7 | Ibex | ~10K | +5.9% | -99.3%
Sky130 | Microwatt | 162K | +51.0% | -99.7%

## Slide 28
ECO Effectiveness Leaderboard
ECO | Applications | Success | Rate
hold_repair | 101 | 101 | 100%
aggressive_timing | 99 | 99 | 100%
multi_pass_timing | 97 | 97 | 100%
buffer_insertion | 77 | 77 | 100%
gate_cloning | 76 | 0 | 0%
dead_logic_elim | 72 | 0 | 0%

## Slide 29
ECO Success by Category
Category | ECOs | Success
Repair | hold, sequential, design, tie_fanout | 100%
Timing | aggressive, multi_pass, full_opt | 100%
Cell | resize, swap, buffer insert/remove | 100%
Placement | timing_driven, density, iterative | 100%
Failed | gate_cloning, dead_logic_elim | 0%

## Slide 30
Key Noodle2 Features Demonstrated
Parallel Execution - Ray-based trial parallelism
Prior Learning - ECO effectiveness tracking
Checkpoint/Rollback - Recovery from degradation
Degradation Detection - Stage 6 flagged without rollback
Multi-PDK Support - Nangate45, ASAP7, Sky130
Safety Domains - Sandbox, guarded, locked modes

## Slide 31
Conclusions
Noodle2 improved timing on **3 different PDKs**
162K cell Microwatt achieved 51% WNS, 99.7% violation reduction
All executions used **real OpenROAD** - no simulation
Prior learning effectively filters ineffective ECOs
System scales from 10K to 160K+ cells
Key insight: ECOs excel at fixing most violations;
worst path(s) may require architectural changes
Total: 1,500 real ECO trials executed

## Slide 32
Thank You
Noodle2 - Physical Design ECO Orchestration
Yaakoub Elkhamra, PhD
All visualizations from actual OpenROAD execution data